## Slide 1
Magnet, Insertion Devices, and MPS Program for K-4GSR
Dong-Eon Kim on behalf of Magnet, ID team,
4GSR Research Division,
Pohang Accelerator Laboratory,
POSTECH, KyungBuk, Republic of Korea
Nov. 5 2025

## Slide 2
Contents and Background
Magnet System for K-4GSR
  Short summary of “routine” magnet
  PM based LGBM development
  Single sided dipole quadrupole (DQ51) development.
  Booster Combined Dipole Development
ID development status for K-4GSR.
MPS system status for K-4GSR
Summary
1

## Slide 3
Magnet Summary for Booster and SR
Magnet | Required Number | Remark
Central BM | 28 | 1*28
Long. BM | 112 | 4*28
Reverse Bend | 168 | 2*3*28 (should have B, B’)
Quad Bend | 56 | 2*28 (should have B, B’)
Quadrupoles | 344 | 6*2*28+8
Sextupoles | 168 | 6*28 (should have B”, H/V Corr, Skew Quad)
Octupole | 56 | 2*28
Fast Corr. | 112 | 4*28 (H/V combined corrector)
Magnets/Sec | 35 | 31+4 (fast Corr.)
Total | 1,044 | Total number of magnets
Magnet | Required Number | Remark
Combined Dipole | 60 | 56 (6.07deg)+4(5.02deg)
Quadrupole | 66 | 
Sextupoles | 60 | 
Corr. | 240 | H120, V120
Total | 426+ | Total number of magnets
Booster Magnet Summary
SR Magnet Summary

## Slide 4
Magnet System – Storage ring
LGBM
CB
Dipole-Quadrupole
(DQxx, 56ea)
Quadrupole
(Qxx, 344ea)
Sextupole
Sxx, 168ea)
Octupole
(Oxx, 56ea)
H/V/S Corrector
(Cxx, 112ea)
(456 magnets for booster)
1576+
Magnets | Required Number | Remark
Center BM (2T) | 28 | 1*28
Long. BM | 112 | 4*28
Reverse Bend | 168 | 2*3*28 (should have B, B’)
Quad Bend | 56 | 2*28 (should have B, B’)
Quadrupoles | 344 | 6*2*28+8(QH)
Sextupoles | 168 | 6*28 (should have B”, H/V Corr, Skew Quad)
Fast Corr. | 112 | 4*28 (H/V combined corrector)
Octupole | 56 | 2*28
SUM | 1044 | Total number of SR magnets

## Slide 5
5
Booster Ring Magnet System
Sextupole
(BS, 60ea)
Corrector
(BCH, 120ea)
Combined Bending Magnet
(BD, 60ea)
Quadrupole
(BQ, 66ea)
Quadrupole Skew
(BQs, 10ea)
Corrector
(BCV, 120ea)
Magnets | Required Number | Remark
Combined Dipole | 60 | 56 (6.07deg)+4(5.02deg)
Quadrupole | 76 | Normal 66, Skew 10
Sextupoles | 60 | 
Corr. | 240 | H120, V120
Sum | 436+ | Total number of magnets
BD
BC H/V
BQs
BS
BQ
BC H/V
BQ
BC H/V
BD
BS
BC H/V
One-cell Layout of Korea-4GSR Booster ring
Circumference : 772.893 m
If separate function dipole is used, the cost of magnet will increase significantly due to the length of the booster.
(Answer to the Dr. Chen’s advice)

## Slide 6
Mechanical designs are fixed with specified I, V.
Voltage rating is for DC excitation and depend on the operation/connection scenarios.
Dipole is straight core, parallel faced to facilitate manufacturing and magnetic measurements.
Initially, 4 multi-filar connection is assumed, to ease the timing issues. But it changed to serial connection of 14 magnets after Dr. Chen’s advice.
Dipole coils can be 2 pancakes/coil (24 turns), or 1 wound coils/coil ( ~23 turns). It depends on the manufacturing concept.
Booster Magnet Overall Summary

## Slide 7
General Design Requirements
LGBMs mirror symmetric in longitudinal direction with respect to center bend.
Dipole Quadrupole (DQ) series operational range is 95% to 105% of the nominal value.
Quadrupole operational range is 75% to 110% of the nominal value.
Sextupole magnets operational range is 50 to 120% of the nominal value.
More than 98% magnetic efficiency for sextupole for min cross-talk btw the H/V/SQ coils.
DQ, Quads should have 90% min efficiency.
Coolant pressure drop is 6bar (or 90 psi) with inlet temperature of 25C.
Coolant temperature rise is limited to less than 20 K.
Min H/V apertures are decided based on BD simulation and vacuum requirements.
Typical Quad aperture radius is 15 mm with good field radius of 10.0 mm except DQ51, DQ32.
DQ51 ro/rc=7 mm/30 mm, DQ32 ro/rc=7 mm/20 mm, Good Field Radius is at offsetted position.
For Quadrupoles, multipole requirements are < 1.0E-3 at good field radius.
For Sextupoles ro/rc=10 mm/20 mm with multipole < 1.0E-3 at good field radius.
For Dipoles, the uniformity requirement is DB/B < 1.0E-3 for +-13.0 mm.
Vertical half gap for center bend, LGBMs are 7.0/12.5 mm, respectively.
Fast correctors need about 0.370 H/V mrad kick.

## Slide 8
DQ and Quadrupole Magnet
3D FEM Model
B’ along the magnet
B6, Before (black), Red (after) end chamfering
Quad, and DQ magnets are similar design. Two DQ types have longer effective length and decided to be arc shape. Other quad, DQs have straight core shape.
Apertures are all 15 mm for quad, and 15, 20, 30 mm for DQ magnets.
The fundamental component, and two first allowed harmonics B6, B10 along the magnet is calculated for each 1 mm slices which were well within requirements.
Pole shape is optimized in 2D, end chamfering is optimized for 3D effects.
Each quadrupole and DQ types have different photon exit slot size.
y=2.0057z
z=rc/3
rc=15 mm
Tan(63.5o)=2.0057

## Slide 9
Sextupole Magnets
Cross talk between Sextupole components and other components
Vacuum requires minimum 13.0 mm gap between the poles.
This seriously restricts pole width and therefore increases multipole errors.
Unlike quadrupole, tangential shims are introduced in real plane resulting flat pole shape to achieve maximum b9 corrections.
Max B”=2084 T/m2, with effective length 200 mm, 180 mm. Aperture is increased to 20 mm to accommodate the vacuum requirements.
All sextupoles should have H-corr/V-corr/Skew Quad windings.
H/V correctors should be able to kick 0.6 mrad@4Gev
Skew Quadrupole larger than 1.0 T/m.
The impact of the interference between the components are shown in the above graph. Even at full excitation, we can expect 96% strength.

## Slide 10
 | Unit | H-Corrector | V-corrector
max kick | rad (DC) | 3.70E-04 | 3.70E-04
B0= | T | 4.11E-02 | 3.01E-02
Leff= | m | 1.22E-01 | 1.20E-01
Req. BL= | Tm | 4.93E-03 | 4.93E-03
Center hgap | mm | 16.0 | 16.0
Right hgap | mm | 12.5 | 12.5
Left hgap | mm | 12.5 | 12.5
NI/pole= | A | 574.4 | 1217.7
core_len= | m | 0.070 | 0.070
Ac= | m2 | 8.55E-06 | 8.550E-06
jmax= | A/mm2 | 1.56 | 2.13
I= | A | 13.3 | 18.1
N/coil= | turns | 43 | 67
Ncoil= |  | 2 | 4
P (total)= | Watts | 9.4 | 46.4
V= | Volts | 0.70 | 2.55
R= | Ohm | 0.053 | 0.140
L = | Henry | 0.0078 | 0.0081
Major Parameters and 3D drawings
Inductances minimized for FOFB. (Thick conductor, less turns)
Maximum DT ? Since air cooling and high Jc~ 2.07 A/mm2.
Recent prototype DT test showed about ~20K DT.
H/V Corrector Magnet

## Slide 11
O31

## Slide 12
θ=3.3564 mrad
θ=4.1690 mrad
Apex s0=0.850037 m
Apex s0=0.742563 m
LGBM2
LGBM1
Actual magnets should satisfy the total bending angle, and apex points to meet the lattice requirements
Orbit
Orbit
Ideal Field profile, Apex points of LGBM1, LGBM2

## Slide 13
Field tuning using FeSi (sheet, bolt), and Temperature Compensation scheme
FeNi for DT compensation
Sm2Co17 Magnet
FeSi for field tuning
FeNi (DT compensation), FeSi (Field level adjustment) plate, bolts are used.
FeNi material property from VAC for T=23, 28 C are applied to assess the temperature compensation.
Magnetic property of Sm2Co17 Br=1.10 T is used conservatively. Thus M1 is designed slightly more than the specification, presuming negative tuning.
Field tuning experiments using FeSi shunts. DB is proportional to the FeSi contact area (sheet, or bolts).
Also for last modules (M1, M5) slidable flux shunts is installed for additional tuning.
ΔB for two FeSi Contact Area (Two bolts, 4 bolts)

## Slide 14
T dependence of BH curve of Thermoflux55/100-G (FeNi)
Curie Temp=55 oC, Flux density at 20oC=0.22 T
Polarization T curve of Thermoflux 55/100-G
Optimum FeNi thickness depending on the central peak field.
T Compensation of Sm2Co17, Calculation of the Required FeNi Thickness
Mechanism for DT compensation of FeNi (Thermoflux)
Higher Temperature >> Reduction in Sm2Co17 magnet Br (-3.30E-4/K)
>> Reduced FeNi saturation>>Smaller flux shunts->> Increase Field Strength

## Slide 15
Example of Optimal FeNi thickness simulation
With given thickness of FeNi, three cases are calculated.
1) ΔT=0 K, FeNi BH table@23C
2) ΔT=5 K, FeNi BH table@23C
3) ΔT=5 K, FeNi BH table@28C
FeNi thickness for same field for (1),(3) are determined for optimum thickness.
The thickness of FeNi should be proportional to the main field for optimal compensation
Since we have only 1.0 mm, 2.0 mm thick FeNi, average thickness will be used for actual experiments, maintaining the total required FeNi volume.
Black :ΔB without Δ T compensation
Blue : ΔB for overcompensated case
Red: ΔB for optimal compensated case

## Slide 16
Temperature Impact Test : LGBM2 M3 case
-400 ppm/K
-70 ppm/K
-36 ppm/K
Temperature Dependence of the Sm2Co17 is ~-350 ppm/K.
FeNi plate is placed on the magnet to reduce the temperature dependence.
NMR probe with precision fixture is used to measure the central field of the each module.
Measurement reproducibility is better than 0.05 G.
Temperature of the measurement room changed from 23.5C to 26.5 resulting ΔT= 3.0 K.
for ΔT= 3.0 K, uncompensated ΔB ~ 2.0 G
Uncompensated measurement showed ~-400 ppm/K.
1st try showed ~-70 ppm/K.
2nd try showed -36 ppm/K
Requirements are < 50 ppm/K.
Confirmed temperature compensation mechanism and estimated FeNi quantity agrees with expectations.

## Slide 17
Tilting Experiment : LGBM2 M3 case
To check the roll angle of a magnet, LGBM M3 module is measured with 1.0 mrad tilting.
The By integral is about 71,800 Gcm.
1 mrad tilting should results ΔIx= 71 Gcm.
The difference of 10 measurement average is 69 Gcm which is close to the estimation.
Standard deviation of the Ix measurement about 5 Gcm, which translates to angle measurement error of 0.074 mrad (in rms).
The measured field integral Ix=-20 Gcm is already low enough.
HEPS is measuring the full length magnet (since it’s a straight magnet). What’s the roll angle alignment tolerances? Our BD requires about something like 0.5 mrad.

## Slide 18
LGBM2 Hall probe scan
LGBM2 prototype on the measurement bench.
Hall probe is Senis 3axis integrated sensor.
Measured (black), lattice (red) field profile. The fields are tuned using FeSi plate, and tuning bolts.

## Slide 19
Assembled Single Sided DQ51, and DQ51 on the Hall bench

## Slide 20
DQ51 Field Map, and Calculated orbit, B, B’ along the orbit
Hall probe map and calculated orbit.
Chart: s [mm]
Chart: s [mm]
Field profile along the orbit
B’ profile along the orbit.
2D field map at the midplane is measured using Senis integrated Hall probe sensor at the rated current.
Field level is slightly tuned to produce exact design B’ at the magnet center.
Particle is tracked at the offsetted position for the lattice B value.
Major components B, B’ along the orbit meets the BD requirements.
Estimation of multipole along the curved orbit need to be confirmed.

## Slide 21
4GSR(오창) Magnetic Measurement LAYOUT
• 4GSR magnet Measurement System: Hall probe, Stretched wire, Vibrating wire, PCB Rotating coil are planned.
• ID clean room magnetic measurement system: SAFALI like in-situ system will be prepared..
• Calibration room : Reference magnet, NMR Probe, Helmholtz Coil will be prepared
< Stretched wire system >
< Hall probe system >
< Rotating coil system >
< Undulator measurement system >
< Calibration system >

## Slide 22
Most important dipole magnet design is completed.
Combined magnet with quad components wit 0.5 mm lamination (2 Hz operation)
Straight core to facilitate manufacturing and magnetic measurement (like Sirius)
Pole width became wider due to the sagitta.
Booster Dipole
22

## Slide 23
23
4GSR: Booster Dipole Parameters
Dipole (Weak, Strong) parameters are listed.
There are 4 slightly weaker magnet for racetrack positions. (Parameters are similar). Total required magnets is 60.
Magnet has 2 independent coils and 14 magnets are connected in alternating sequence (4 MPSs for 56 magnets, additional two MPSs for 4 weak dipoles).
Inductances (Number of turns) are tuned for MPS requirements to limit the maximum voltages.
Lamination is 0.5 mm thick Silicon steel with low coercivity to minimize the remanence fields. 98% packing factor is assumed. IHEP supplied actual BH table for the material.
Conductor size 13 mm x 13 mm square with 6.5 mm cooling hole.
2 in/out terminals for each magnet.
 | BD Weak (Ext) | BD Strong (Ext) | Unit | Remark
Magnet type | parallel face | parallel face |  | 
Shape along the beam | straight | straight |  | 
Lamination thickness | 0.5 | 0.5 | mm | 
Number of Magnets | 4 | 56 | EA | 
bending angle | 5.02 | 6.07 | degree | 
rc or half gap | 0.0137 | 0.0137 | m | 
Brho= | 13.3426 | 13.3426 | Tm | 
BL= | 1.16902 | 1.41353 | Tm | 
Leff= | 1.42155 | 1.42155 | m | 
B0= | 0.8224 | 0.9944 | Tesla | 
B'= | -1.45572 | -1.76019 | T/m | 
B' Leff = | 2.0694 | 2.5022 | T | B0*tan(theta/2)*2
B' Leff (edge)= | 0.0721 | 0.1054 | T | 
B' Leff (total)= | 2.1415 | 2.6076 | T (Along orbit) | 
rho= | 16.225 | 13.418 | m | 
sagitta= | 0.0156 | 0.0188 | m | 
L_core= | 1.3960 | 1.3960 | m | 
Efficiency= | 0.97 | 0.97 |  | 
Ampere turns/coil= | 9,242.7 | 11,175.9 | Aturn | 
Total Power (1 magnet)= | 3,386 | 4,951 | Watts | 
Conductor Geometry | 13 mmx 13 mm with 6.5 mm hole |  | mm | 
Number of Turns= | 24 | 24 |  | might change to 23
Number of cooling channel= | 2 | 2 |  | 
Inom= | 385.1 | 465.7 | A | 
jeff= | 2.85 | 3.45 | A/mm2 | 
Voltage Drop/magnet= | 8.79 | 10.63 | Volt | 
Resistance/magnet= | 0.023 | 0.023 | Ohm | 
Coolant DT= | 2.3 | 3.4 | K | 
Resistive Voltage Drop Total= | 17.6 | 148.8 | Volts | 
Inductive Voltage | 54.0 | 457.4 | Volts | 
Duty (Power)= | 0.321 | 0.321 |  | 
DI/DT (Max)= | 1463.4 | 1769.5 | A/sec | 
Inductance (3D) (All coils)= | 0.0185 | 0.0185 | Henry | 95%Inom in 0.25 sec

## Slide 24
Pole optimization using conformation map: Jack Tanabe
(U, V) plane
(X,Y) plane
Instead of optimizing in (u,v) plane, after introducing shims, real geometry is calculated with real BH curve evaluating the uniformities.
Chart: DB/B
| -2.4E-2 | -2.24E-2 | -2.0799999999999999E-2 | -1.9200000000000002E-2 | -1.7600000000000001E-2 | -1.6E-2 | -1.4400000000000001E-2 | -1.2800000000000001E-2 | -1.12E-2 | -9.6000000000000009E-3 | -8.0000000000000002E-3 | -6.3999999999999994E-3 | -4.8000000000000022E-3 | -3.2000000000000015E-3 | -1.6000000000000007E-3 | 0 | 1.6000000000000007E-3 | 3.199999999999998E-3 | 4.7999999999999987E-3 | 6.3999999999999994E-3 | 8.0000000000000002E-3 | 9.5999999999999974E-3 | 1.1200000000000002E-2 | 1.2799999999999999E-2 | 1.4399999999999996E-2 | 1.6E-2 | 1.7599999999999998E-2 | 1.9200000000000002E-2 | 2.0799999999999999E-2 | 2.2399999999999996E-2 | 2.4E-2
 | -0.00055844 | 0.00018832 | 0.00042095 | 0.00039748 | 0.00030391 | 0.00020741 | 0.00013525 | 8.4521e-05 | 5.229e-05 | 3.2718e-05 | 2.0936e-05 | 1.3048e-05 | 7.1084e-06 | 4.0897e-06 | 1.0711e-06 | 0 | -1.0711e-06 | -1.9475e-07 | 2.6291e-06 | 9.348e-06 | 2.0936e-05 | 4.1287e-05 | 7.3323e-05 | 0.00012581 | 0.00019874 | 0.00029358 | 0.00038979 | 0.00043809 | 0.00032465 | -0.00014431 | -0.0012012
 | -0.0012457 | -0.00020375 | 0.00026053 | 0.00038687 | 0.00037567 | 0.00031044 | 0.00023538 | 0.00016917 | 0.00011671 | 7.8984e-05 | 5.1084e-05 | 3.1044e-05 | 1.7879e-05 | 8.645e-06 | 3.3401e-06 | 0 | -3.9296e-07 | 4.126e-06 | 1.2575e-05 | 2.6917e-05 | 5.1084e-05 | 8.5075e-05 | 0.00013292 | 0.00019441 | 0.00026387 | 0.00032773 | 0.00034904 | 0.00026986 | -3.3598e-05 | -0.00074455 | -0.0020731





Uniformity for several shims

## Slide 25
Booster Dipole : B and B’ along the orbit (Based on the 3D calculations)
B [T] along the orbit. At z=0 electron is located in the weaker region. (Magnet is straight, orbit is curved)
B’ [T/m] along the orbit. The B’ has a steep drop at the edge. The effective length for quadrupole component is shorter than the dipole component.
Also edge contribution is clearly shown.
The total integrated B, and B’ should match the lattice specifications instead of center value.

## Slide 26
Based on the real orbit
Pure Arc Version
Reference orbit change due to the combined bending magnet
Reference orbit of the booster is redrawn based on the orbit calculated from the 3D field.
The orbit differs from the previous pure arc version by 0.106 mm~0.109 mm. (Real orbit is outside of the old arc based orbit).
These change is reflected in the location of all booster magnet position.

## Slide 27
Booster Quadrupole is rather simple magnet, with aperture radius 18.0 mm, effective length 200 mm, B’max=29 T/m, 66 are required.
A small number of weak skew quadrupoles are also required. It will be 45degree rotated version of a normal quadrupole magnet.
Booster Quadrupole
27

## Slide 28
2 EPU (EPU78, EPU98) : out-sourced
8 IVU : period 16~24 mm, min gap=5.0 mm, magnetic Length=~ 3.0 m.
Major upgrade from PLSII IVU20.
  -Min operational gap 6.0 mm -> 5.0 mm
  -More kinds of period: 20 mm -> 16, 20, 22, 24 mm
  -Length change: 1.8 m -> 3.0 m (magnetic length)
  -In situ measurement system ready
  -Parabolic gap deformation designed to be < ±3 μm to meet δφ <5o for all working gaps.
  -Contract awarded for 8 IVUs to a domestic company.
10 Undulator Sources are assumed for 1st phase beamline

## Slide 29
2 conventional EPU undulator, an EPU98, and an EPU78. We already have a contract.
Main parameters | EPU78 | EPU98
Undulator type | APPLE-II type Elliptically Polarized Undulator (EPU) | APPLE-II type Elliptically Polarized Undulator (EPU)
Longitudinal Symmetry | Anti Symmetric | Anti Symmetric
Entrance/Exit Sequence | +-1/4,-+3/4,+-1,-+1,… | +-1/4,-+3/4,+-1,-+1,…
Control System | EPICS Ready | EPICS Ready
Possible Operation Mode | Parallel/Anti Parallel | Parallel/Anti Parallel
Up/Downstream Correctors | H/V correctors at the UP/Down stream with MPS | H/V correctors at the UP/Down stream with MPS
Magnet block material | VACODYM 863 or Equivalent Br > 1.25 T , HcJ > 2000 kA/m | VACODYM 863 or Equivalent Br > 1.25 T , HcJ > 2000 kA/m
Period length λu | 78.0 mm | 98.0 mm
Block Dimension (W/H/T) 5 mm recess for clamping | 35.0 mm (W) /30.0 mm (H)/19.5 mm (T) | 35.0 mm (W) /30.0 mm (H)/22.5 mm (T)
Number of full field Period | 23 (For Pure Vertical field planar mode) | 36 (For Pure Vertical field planar mode)
Number of full field poles | ≈46 | ≈72
Total number of poles | ≈46+transition sequence | ≈72+transition sequence
Undulator length at zero phase (planar mode) | ≈1794 mm + transition sequences | ≈3528 mm + transition sequences
Operating Gap range | 15~100 mm | 15~100 mm
Max Maintenance Gap | 260 mm | 260 mm
Effective field for vertical field polarization (Byeff ) | >0.954 T (Array Phase=0) | > 1.009 T (Array Phase=0)
Effective field for circular mode (Byeff=Bxeff) | >0.602 T | > 0.663 T
Effective field for horizontal polarization (Bxeff) | >0.776 T (Array Phase= λu /2) | > 0.880 T (Array Phase= λu /2)
Phase error for all working gaps | < 5° rms | < 5° rms
Key Parameters of the EPUs

## Slide 30
Magnet Power Supply optimization:
3 types of reverse-bends, 5 types of quadrupoles, and 3 types of sextupoles use the same type of power supply. (U,140A / 40V, UNIDC MPS)
Among them, 1 type of center-band and 1 type of quad-bend are connected in parallel to increase current capacity.
the embedded correctors, fast correctors, skew sextupoles, octupoles, trims of quad-bands use the same type of power supply. (B, 20A / 20V, BIDC MPS)
In total, we have only 2 kinds of PS for the Storage Ring machine
Design Concept of MPS for SR
Goal:
Minimize the number of power supply types for many different magnets and use a modular structure to enable parallel operation, increasing current capacity.
Makes maintenance and spare parts management easier.
Lower costs through mass production of same type modular MPS.
Fewer types of MPS also allow us to focus on design optimization.

## Slide 31
Specifications | UNIDC MPS | BIDC MPS
Maximum Current | + 140 A | ± 20 A
Maximum Voltage | + 40 V | ± 20 V
Maximum Power | 5.6 kW | 400 W
Topology | Unipolar | Bipolar (Full-Bridge)
Small Signal Bandwidth (-3dB) | > 1 kHz | > 10 kHz
Current Accuracy | < 100 ppmP-P / FS | < 100 ppmP-P / FS
Stability | ≤ 10 ppmRMS (8 hr) / FS | ≤ 30 ppmRMS (8 hr) / FS
Line & Load Regulation | < ± 40 ppmP-P | < ± 50 ppmP-P
Cooling | Air (front-to-rear) | Air (front-to-rear)
Efficiency | > 85% @full load | 
Power Factor | > 0.98 @full load (with Active Power Factor Correction) | 
PARALLELING | Up to 4 modules | No Parallel Required
Input Ratings | Three-phase : 380 VAC /60 Hz (±10%) | Single-phase : 220 VAC /60 Hz (±10%)
SR MPS Specification
Remark:
Two supplier developed prototypes independently and finished test.
The procurement scope includes 2700+ MPS (SR, Booster, Septum, LTB, BTS), with installation.
The procurement will be in RFP format, and 3 domestic companies and one foreign companies are expected to participate.

## Slide 32
Booster Ring Bending Magnet Wiring Scheme
Two hollow conductor forms one terminal. (Bifilar connection)
Instead of old 4 parallel connection, changed to series connection.
Practically, one supply powers 14 dipoles in an alternate position.
Alternate connection was selected because the location of the power supplies are located in the same position.
Symmetric wiring to reduce common mode noise. (U-U...-D-D...) (JPARC and experiences in other labs)

## Slide 34
Summary
Most of the K-4GSR SR magnets contracts will be done within this year.
(Only DQ51, DQ52, LGBM1 remains to be contracted within this year).
Booster magnets design complete, and expected to be contracted early next year.
Thick septum short version prototype successful.
Procurement for LTB, BTS, Septum magnets will follow soon.
8 In Vacuum Undulators are already awarded to domestic company.
We have an additional contract for 2 EPUs to foreign company (Kyma).
MPS system is targeting modular structure for a productive serial production, and a easier maintenance.
Prototyping for a unipolar module MPS was successful (including parallel operation).
Procurement for the whole MPS system (including installation) is in progress and is expected to be finished within 2025.

## Slide 35
Thank You

## Slide 36
Backup Slides

## Slide 37
BEAM
BEAM
Key Quantities | CBM-Q52 | L1(M1)-Q12 | L1(M5)-32 | L2(M1)-Q32 | L2(M5)- Q51
Key Quantities | CBM-Q52 | L1(M1)-Q12 | L1(M5)-32 | L2(M1)-Q32 | L2(M5)- Q51
L1 and L2 denote LGBM1 and LGBM2, respectively.
Representative results are presented for CBM and LGBM2-M5 among five simulated dipole cases (CBM, LGBM1–M1/M5, LGBM2–M1/M5).
In the tracking plots, the black line indicates the beam trajectory.
1. Center Bending Magnet (CBM)
Opera 3D Modeling
Tracking and field map
Multipoles
2. Longitudinal Gradient Bending Magnet 2 Module 5 (LGBM2-M5)
Opera 3D Modeling
Tracking and field map
Multipoles
Dipole Magnets

## Slide 38
Representative results are presented for DQ32–O31 among other cases.
Cross-talk effects—such as penetration of into neighboring magnet, off-centering caused by the quadrupole fringe field, sextupole-induced —are negligible in most cases.
However, for O31, a quadrupole component appears at O31 due to DQ32 and is significant ().
BEAM
Opera 3D Modeling
Tracking and field map
Multipoles
DQ32 – Octupole (O31)
at O31
Other Magnets

## Slide 39
Photon Source | Ty. | Periods length [mm] | Total Length [m] | Photon Energy(keV) | # | Applicable BL | Beam Port
Bending Magnet | BM |  |  | 5 ~ 100 | 1 | #09. HEMicroscopy | BM10
Out-vacuum Undulator | EPU | 78 | 2 | 0.1 ~ 3.2 | 1 | #03. Soft X-ray NanoProbe | ID26-2
 |  | 98 | 3.6 | 0.05 ~ 2 | 1 | #04. NanoARPES | ID25
In-Vacuum Undulator | IVU | 20 | 3 | 5 ~ 40 | 2 | #06. CoSXAS | ID04
 |  |  |  |  |  | #08. BioNX | ID22
 |  | 22 | 3 | 3 ~ 40 | 1 | #05. CoXRS(CDI) | ID03
 |  | 24 | 3 | 3 ~ 40 | 4 | #01. BioPharma. | ID21
 |  |  |  |  |  | #02. Mat. Structure | ID24
 |  |  |  |  |  | #07. Realtime XAFS | ID23
 |  |  |  |  |  | #10. NanoProbe | ID10
 |  |  | 1.5 | 2 ~7 | 1 | #03. Soft X-ray NanoProbe | ID26-1
Photon Sources
9 ID BL + 1 BM bL, 1 ID BL is canted ID line and requires an IVU and EPU. Total ID required is 2 EPU+ 8 IVU, Period can change

## Slide 40
Input part: The input stage uses SMPS or PFC with a DC/DC converter for isolation and a power factor of 0.98 or higher.
Inverter part:
  Used SiC FET main switches
Output filter part:
  To suppress high frequency ripple, Composed of Preag low-pass filter.
Control part:
  Used FPGA(ZYNQ) & DSP(28337)
  ZYNQ(ARM core & FPGA): Web server & ADC signal processing & Faults
  DSP(TI 28337D): PI control & HR-PWM functionality
Topology of SR magnet power supplies :
Fig. UNIDC MPS (U,140A/40V)
Fig. BIDC MPS (B,20A/20V)
SR MPS Topology

## Slide 41
Sm2Co17 Block Measurements
4 types of PM delivered. (Full Top, Quarter Top, Full side, Quarter Side: FT, QT, FS, FQ)
For example, block measurement results for Full Top (FT) blocks are shown.
There is a difference between batches.
For the prototype, magnets from MagSound is used. For serial production, HPMG Magsound are both considered.
  Costs are comparable, but infrastructure looks better for HPMG (Thanks for the recommendation).
Chart: ax, ay [Degree]
Chart: μMz [T]
Main component (μ0Mz)
X angle, vs Y angle [degree]
Different Batch

## Slide 42
LGBM2 3D FEM Calculation and Analysis
Opera 3D FEM Model
Black line is ideal field profile from Beam Dynamics, and red line is the 3D calculated By profile.
Matching of the 1st integral, 2nd integral (Apex Point) are important, and a marginal difference in the ideal/real profile has very small impact in the beam dynamics according to BD group study, and APS-U Study.

## Slide 43
Photograph of the Final Assembled of LGBM2 Magnet

## Slide 44
Chart: By [z]


Chart: By [z]
Impact of separation between the modules DZ=5,10,15,20 mm.
Single Module vs 5 module field profiles showing cross talk between the modules. (DZ=5mm).
Cross talk between the module are significant.
Tuning using FeSi Shunt is always decreasing direction (design should be higher than the rated value).
Final Field profile is also decreased by FeNi plate application (impact smaller than FeSi).
Additional tunable shunting using Steel Bolt is also assumed (implemented in the design) (Results of HEPS visit).
The final field profiles should have desired bend angle, apex positions, minimal deviation from the ideal orbit (~80 μm).
3 D FEM Modelling
44

## Slide 45
LGBM– PM Version: Sm2Co17 ΔT Compensation, For Sm2Co17 Δ B/B/ Δ T=-3.3E-4/K

## Slide 46
PM Block Assembly Jig
Installing strong Sm2Co17 magnets in the ferromagnetic pole, yoke assembly was a risky procedure
Special tooling for installation of the magnets are designed/implemented successfully.

## Slide 47
Parameters | Electric Excitation |  | Permanent Magnet Version | Remark
 | LGBM1 | LGBM2 |  | 
Magnet Type | LGBM1U/LGBM1D | LGBM2U/LGBM2D | Same | －
Required number | 28/28 | 28/28 | Same | －
B range | 0.7343 T~0.1504 T | 0.3121 T~0.1535 T | Same | －
Uniformity | < 1.0E-3 | < 1.0E-3 | Same | < ±13.0 mm
Min pole gap | 26.0 mm | 24.4 mm | Changed | 25 mm
Magnetic Length | 2.0505 m | 1.9847 m | Same | －
Trim winding | Yes | Yes | NA | -
Max Ampere Turns | 8.45 | 3.17 | NA | kA (per pole)
Conductor | 7.5 × 7.5 × 4.0𝜙 | 8.0 × 8.0 × 5.0𝜙 | NA | unit in mm
Num. Turns | 8, 2, 4, 8, 18 | 7, 1, 1, 2, 3 | NA | high field → low field
Imax | 211.2 | 226.1 | NA | A, 개별 powering
Js | 4.932 | 5.198 | NA | A/mm2
V | 12.7 | 8.83 | NA | V (per magnet)
Power | 2.70 | 2.00 | NA | kW (per magnet)
Pressure drop | 6.0 | 6.0 | NA | bar
Number of Cooling Circuit | 4 | 2 | NA | per magnet
Flow rate | 3.09 | 2.42 | NA | liter/min
ΔT | 8.3 | 6.5 | NA | K (for Δp=6.0 bar)
Comparison of EM version of LGBM and PM based LGBM

## Slide 48
1 pair (LGBM1, LGBM2) prototype worth quantities of Sm2Co17 already delivered
All modules have same cross section, but different PM distributions.
4 Types of PM(Full size Top :FT, Full Size Side : FS, Quarter size Top: QT, Quarter size Side : QS) will be used depending on the module.
1 Module CAD Modelling and Assembled Photo

## Slide 49
LGBM1– PM Version: Full 3D Modeling
Current status: Sm2Co17 block delivered, prototyping in progress.
M1
M2
M5
M4
M3

## Slide 50
(SR Magnet Overall Summary)
Magnet Type | Magnet Name | Qty/Sec | Total | Half Gap Or Radius [mm] | Good Field Rc [mm] | Mag Len. [mm] | Core Lengh [mm] | Max Strength, B,B',B",B''' | Mult or Uniformity [1E-4] | Photon V. Fan | Lam. Or Solid | Trim Winding | Trim Winding Strength | I[A] | V[V] | Remark | Status
Longitudinal Gradient Bending Magnet | LGBM1U | 1 | 28 | 13.9 | ±13mm |  |  | 0.7343~ | 10 | C-type | Sol. | 2nd Int | Yes | 211.2 | 12.75 | Parallel face. Wedged spacer | 
 | LGBM2U | 1 | 28 | 12.2 | ±13mm |  |  | 0.3051~ | 10 | C-type | Sol. | 2nd Int | Yes | 226.1 | 8.83 | Parallel face. Wedged spacer | 본제품 구매완료
 | LGBM2D | 1 | 28 | 12.2 | ±13mm |  |  | 0.3051~ | 10 | C-type | Sol. | 2nd Int | Yes | 226.1 | 8.83 | Parallel face. Wedged spacer | 본제품 구매완료
 | LGBM1D | 1 | 28 | 13.9 | ±13mm |  |  | 0.7343~ | 10 | C-type | Sol. | 2nd Int | Yes | 211.2 | 12.75 | Parallel face. Wedged spacer | 
Center Bend | CB | 1 | 28 | 7.0 | ±13mm | 186.0 | 187.0 | 1.9942 | 10 |  | Sol. | None |  | 228.5 | 7.15 | Parallel faced. | 본제품 구매완료
Quad-Bend and Reverse Bend | DQ31U | 1 | 28 | 15.0 | 7.0 | 200.0 | 189.3 | 58.1 | 10 |  | Sol. | V-Dipole | 3.42A/2.57V | 119.1 | 8.1 | Straight Magnet | 장검위 자료작성중
 | DQ32U | 1 | 28 | 20.0 | 7.0 | 145.0 |  | 26.1 | 10 |  | Sol. | V-Dipole | 3.02A/1.87V | 119.8 | 5.26 | Straight Magnet | 
 | DQ51U | 1 | 28 | 30.0 | 15.0 | 820.0 |  | 26.4 | 10 |  | Sol. | V-Dipole |  | 225 | 28.7 | Curved Pole Tip | 시제품 추진중
 | DQ52U | 1 | 28 | 15.0 | 7.0 | 626.0 |  | 52.0 | 10 |  | Sol. | V-Dipole |  | 102.4 | 17.31 | Curved Pole Tip | 시제품 추진중
 | DQ52D | 1 | 28 | 15.0 | 7.0 | 626.0 |  | 52.0 | 10 |  | Sol. | V-Dipole |  | 102.4 | 17.31 | Curved Pole Tip | 시제품 추진중
 | DQ51D | 1 | 28 | 30.0 | 15.0 | 820.0 |  | 26.4 | 10 |  | Sol. | V-Dipole |  | 225 | 28.7 | Curved Pole Tip | 시제품 추진중
 | DQ32D | 1 | 28 | 20.0 | 7.0 | 145.0 |  | 26.1 | 10 |  | Sol. | V-Dipole | 3.02A/1.87V | 119.8 | 5.26 | Straight Magnet | 
 | DQ31D | 1 | 28 | 15.0 | 7.0 | 200.0 | 189.3 | 58.1 | 10 |  | Sol. | V-Dipole | 3.42A/2.57V | 119.1 | 8.1 | Straight Magnet | 장검위 자료작성중
Quadrupole | QH1U | 1 | 2 | 15.0 | 10.0 | 200.0 | 189.3 | 16.3 | 10 |  | Sol. | None |  | 34.90 | 2.50 | 145 mm: 112 | 장검위 자료작성중
 | QH2U | 1 | 2 | 15.0 | 10.0 | 200.0 | 189.3 | 28.0 | 10 |  | Sol. | None |  | 59.89 | 4.30 | 200 mm: 124+56 (DQ31) | 장검위 자료작성중
 | QH3U | 1 | 2 | 15.0 | 10.0 | 200.0 | 189.3 | 44.5 | 10 |  | Sol. | None |  | 95.25 | 6.84 | 250 mm: 52 | 장검위 자료작성중
 | QH4U | 1 | 2 | 15.0 | 10.0 | 200.0 | 189.3 | 18.0 | 10 |  | Sol. | None |  | 38.55 | 2.77 | 384 mm: 56 | 장검위 자료작성중
 | Q11U | 1 | 26 | 15.0 | 10.0 | 250.0 | 239.3 | 49.4 | 10 |  | Sol. | None |  | 105.80 | 8.79 | 112 | 장검위 자료작성중
 | Q12U | 1 | 26 | 15.0 | 10.0 | 200.0 | 189.3 | 41.7 | 10 |  | Sol. | None |  | 89.33 | 6.41 | 124 | 장검위 자료작성중
 | Q31U | 1 | 28 | 15.0 | 10.0 | 145.0 | 134.4 | 56.2 | 10 |  | Sol. | None |  | 120.40 | 7.13 | 52 | 장검위 자료작성중
 | Q32U | 1 | 28 | 15.0 | 10.0 | 145.0 | 134.4 | 56.2 | 10 |  | Sol. | None |  | 120.40 | 7.13 | 56 | 장검위 자료작성중
 | Q51U | 1 | 28 | 15.0 | 10.0 | 384.0 | 374.0 | 53.6 | 10 |  | Sol. | H/V-corr | 3.4A/5.8V | 114.80 | 13.04 | Q51 0.6 mrad h/v-kick | 장검위 자료작성중
 | Q52U | 1 | 28 | 15.0 | 10.0 | 200.0 | 189.3 | 57.4 | 10 |  | Sol. | None |  | 122.90 | 8.82 |  | 장검위 자료작성중
 | Q52D | 1 | 28 | 15.0 | 10.0 | 200.0 | 189.3 | 57.4 | 10 |  | Sol. | None |  | 122.90 | 8.82 |  | 장검위 자료작성중
 | Q51D | 1 | 28 | 15.0 | 10.0 | 384.0 | 374.0 | 53.6 | 10 |  | Sol. | H/V-corr | 3.4A/5.8V | 114.80 | 13.04 | Q51 0.6 mrad h/v-kick | 장검위 자료작성중
 | Q32D | 1 | 28 | 15.0 | 10.0 | 145.0 | 134.4 | 56.2 | 10 |  | Sol. | None |  | 120.40 | 7.13 |  | 장검위 자료작성중
 | Q31D | 1 | 28 | 15.0 | 10.0 | 145.0 | 134.4 | 56.2 | 10 |  | Sol. | None |  | 120.40 | 7.13 |  | 장검위 자료작성중
 | Q12D | 1 | 26 | 15.0 | 10.0 | 200.0 | 189.3 | 41.7 | 10 |  | Sol. | None |  | 89.33 | 6.41 |  | 장검위 자료작성중
 | Q11D | 1 | 26 | 15.0 | 10.0 | 250.0 | 239.3 | 49.4 | 10 |  | Sol. | None |  | 105.80 | 8.79 |  | 장검위 자료작성중
 | QH4D | 1 | 2 | 15.0 | 10.0 | 200.0 | 189.3 | 18.0 | 10 |  | Sol. | None |  | 38.55 | 2.77 |  | 장검위 자료작성중
 | QH3D | 1 | 2 | 15.0 | 10.0 | 200.0 | 189.3 | 44.5 | 10 |  | Sol. | None |  | 95.25 | 6.84 |  | 장검위 자료작성중
 | QH2D | 1 | 2 | 15.0 | 10.0 | 200.0 | 189.3 | 28.0 | 10 |  | Sol. | None |  | 59.89 | 4.30 |  | 장검위 자료작성중
 | QH1D | 1 | 2 | 15.0 | 10.0 | 200.0 | 189.3 | 16.3 | 10 |  | Sol. | None |  | 34.90 | 2.50 |  | 장검위 자료작성중
Sextupole + Slow corrector | S31U | 1 | 28 | 20.0 | 10.0 | 180.0 |  | 1802.3 | 50 |  | Sol. | H/V/SQ | 8.0A/6.7V | 117.617 | 3.89 | H/V Strength | Solid로 변경 (ESRF, APSU, SLS-II 를 따라서)
 | S32U | 1 | 28 | 20.0 | 10.0 | 200.0 |  | 2083.9 | 50 |  | Sol. | H/V/SQ | 8.0A/7.2V | 117.617 | 4.22 |  | 
 | S33U | 1 | 28 | 20.0 | 10.0 | 180.0 |  | 1419.6 | 50 |  | Sol. | H/V/SQ | 8.0A/6.7V | 117.617 | 3.89 | Not all sex has all the functions | 
 | S33D | 1 | 28 | 20.0 | 10.0 | 180.0 |  | 1419.6 | 50 |  | Sol. | H/V/SQ | 8.0A/6.7V | 117.617 | 3.89 | Pole to pole distance +-6.5 mm 이상. | 
 | S32D | 1 | 28 | 20.0 | 10.0 | 200.0 |  | 2083.9 | 50 |  | Sol. | H/V/SQ | 8.0A/7.2V | 117.617 | 4.22 | independently powered (BD requirements) | 
 | S31D | 1 | 28 | 20.0 | 10.0 | 180.0 |  | 1802.3 | 50 |  | Sol. | H/V/SQ | 8.0A/6.7V | 117.617 | 3.89 |  | 
Octupole Magnet | O31U | 1 | 28 | 15.0 | 10.0 | 80.0 | 74.0 | 240,000 | 200 | C-type | Sol. | None | - | 3.6 | 12.1 |  | 장검위 자료작성중
 | O31D | 1 | 28 | 15.0 | 10.0 | 80.0 | 74.0 | 240,000 | 200 | C-type | Sol. | None | - | 3.6 | 12.1 |  | 장검위 자료작성중
Fast-Slow Corrector | C1U | 1 | 28 | 12.5 | ±10mm | 121.0 | 70.0 | 0.6 mrad | 100 | C-type | Lam0.35 |  |  | 3.0/4.0 | 4.9/16.0 | max 0.6 mrad | 본제품 구매완료
 | C2U | 1 | 28 | 12.5 | ±10mm | 121.0 | 70.0 | 0.6 mrad | 100 | C-type | Lam0.35 |  |  | 3.0/4.0 | 4.9/16.0 | 1% uniformity=100 | 본제품 구매완료
 | C2D | 1 | 28 | 12.5 | ±10mm | 121.0 | 70.0 | 0.6 mrad | 100 | C-type | Lam0.35 |  |  | 3.0/4.0 | 4.9/16.0 | Corrector numb count differ in 4 due to high beta section | 본제품 구매완료
 | C1D | 1 | 28 | 12.5 | ±10mm | 121.0 | 70.0 | 0.6 mrad | 100 | C-type | Lam0.35 |  |  | 3.0/4.0 | 4.9/16.0 |  | 본제품 구매완료

## Slide 51
Lattice Requirements of LGBM1, LGBM2
Chart: LGBM1 ideal profile
| 0 | 0 | 0.16494 | 0.16494 | 0.37107999999999997 | 0.37107999999999997 | 0.83731999999999995 | 0.83731999999999995 | 1.48146 | 1.48146 | 2.0505 | 2.0505
 | 0 | 0.73427 | 0.73427 | 0.43023 | 0.43023 | 0.287 | 0.287 | 0.19726 | 0.19726 | 0.15039 | 0.15039 | 0
Chart: LGBM2 ideal profile
| 0 | 0 | 0.53969999999999996 | 0.53969999999999996 | 0.84729999999999994 | 0.84729999999999994 | 1.3342000000000001 | 1.3342000000000001 | 1.6928000000000001 | 1.6928000000000001 | 1.9847000000000001 | 1.9847000000000001
 | 0 | 0.31216 | 0.31216 | 0.2397 | 0.2397 | 0.20265 | 0.20265 | 0.17327 | 0.17327 | 0.15354 | 0.15354 | 0
LGBM1 | 
L [m] | B [T]
0.1649 | 0.7343
0.2061 | 0.4302
0.4662 | 0.2870
0.6441 | 0.1973
0.5690 | 0.1504
LGBM2 | 
L [m] | B [T]
0.5397 | 0.3122
0.3076 | 0.2397
0.4869 | 0.2026
0.3586 | 0.1733
0.2919 | 0.1535
Each LGBM has 5 step profile like ESRF-ABS, APS-U, HEPS.
The profile is mirror symmetric with respect to the center bending magnet (one weak->strong, other strong->weak). Therefore, upstream/downstream magnet should be carefully designed/assembled.
Each magnet has 5 modules having flat field profile. Each module is parallel faced and have angle relative to the previous module. Total LGBM1 length is 2.0505 m, while LGBM2 is 1.92306 m.

## Slide 52
Key Parameters of Electrically Excited LGBM2/LGBM1 Magnets
Parameter | LGBM1 | LGBM2 | Remark
Magnet Type | LGBM1U/LGBM1D | LGBM2U/LGBM2D | 
Required # | 28/28 | 28/28 | 
B Range | 0.7343T-0.1504T | 0.3121T-0.1535T | 
Uniformity | < 1.0E-3 | < 1.0E-3 | <± 13.0 mm
Min. pole gap | 26.0 mm | 24.4 mm | 
Magnetic Length | 2.0505 m | 1.9847 m | 
Trim winding | Yes | Yes | For 2nd integral control
Max Amper Turns | 8.45 | 3.17 | kA (per pole)
Conductor | 7.5 x7.5 x 4.0𝜙 | 8.0 x 8.0 x 5.0𝜙 | Unit in mm
Num. Turns | 8,2,4,8,18 | 7,1,1,2,3 | From Low F to high F
Imax | 211.2 | 226.1 | A, independent powering
Js | 4.932 | 5.198 | A/mm2
V | 12.7 | 8.83 | V (per magnet)
Power | 2.7 | 2 | kW (per magnet)
Pressure drop | 6 | 6 | bar
Number of Cooling Cir. | 4 | 2 | per magnet
Flow rate | 3.09 | 2.42 | liters/min
ΔT | 8.3 | 6.5 | K (for Δp=6.0 bar)
Required # : 56+4 (1st article+Spare Magnet)
Staggered coil design following APS-U

## Slide 53
Photograph of the Final Assembled of LGBM2 Magnet, Measured Uniformity
Measured Uniformity of the EM version.
X [mm]

## Slide 54
International Advisory Committee (IAC) (Nov 2023)
Machine Advisory Committee (MAC) Recommendations (Nov 2023)

## Slide 55
PM version LGBM Magnet
LGBM has longitudinal field profile ranging from 0.15 T – 0.75 T to minimize beam emittances..
Old design used electric excitation following APS-U for concerns on the long term radiation damage.
But ESRF-EBS operating experience shows no radiation damage after 2 year operation.
2023 MAC (Machine Advisory Committee), IAC recommended to consider PM version also.
PM Version can save energy costs, Assuming, 1 kwh=150 Won, the design change can save 3.0 MWh/year, 7,000 MWon for 20 year operation. (about 4.50 MUSD/20 years)
Also costs for MPS can be saved.
PM version has advantage in designing photon stops due to its smaller physical size
Technical Challenges
No tunability like EM excitation, The final field profile should be met during measurement/tuning stage.
Sm2Co17 PM has a temperature dependence about ΔB/B/ΔT= -3.5E-4/K.
There is cross talk between the modules.
Engineering Solution
Tunability using FeSi (Silicon Steel) shunts. FeSi can be in a sheet form (ESRF), or shunting bolt like HEPS.
(always in decreasing direction).
Weakening of Temperature dependence using FeNi (Ni steel) plate.
Magnetic design taking into account the Cross-talk between the modules.
55

## Slide 56
Initial Design of LGBM and Some history
Initial design of LGBM was electromagnet using “staggered” coils like APS-U
The design was rather straight forward, and it’s already adopted by APS-U.
There were concerns on the long term radiation damage of the Sm2Co17 magnets.
  PLS-II is operating 9 in vacuum undulators based on the Vacuum Schmelze Sm2Co17 magnets.
  Sometimes beamlines complains degradation of the undulator performance and it need deinstall/retuning/reinstallation.
  The re-installation period is not so predictable, but approximately about ~ 6-7 years.
The field profile does not follow the lattice specification exactly. It meets the total bending angle (1st field integral), and apex points (2nd field integral).
The exact shape of the field profile does not affect the beam dynamics of the storage ring. (APS-U experience, and 4GSR beam dynamics simulation confirms it)
1st prototype of eclectically excited LGBM2 is produced and confirmed to meet the requirements.
However, 2023 MAC Dr. Gael Le Bec ESRF commented ESRF-EBS experienced no radiation damage after 2 full year operation.
Also, 2023 Nov IAC, MAC recommended to consider PM based LGBM.

## Slide 57
Integrated Uniformity of each Modules
Requirement is |DB/B| < 1.0E-3 for |x| < 13.0 mm.
Each segment is mapped standalone to characterize the field quality.
Total integrated field uniformity is not good due to the fringe field contribution.
The fringe field contribution will be minimized when all modules are assembled.
Integrated field uniformity of the body region of the each module agrees very well with design.
Errors mostly depend on the pole face parallelism and tapering.

## Slide 58
Field Clamp impact to limit the fringe field
Field clamp experiment:
Black : Without field clamp
Red: Field with field clamp (showing rapid decay)
Blue: Difference between the two cases
Distance to the next magnet core ranges from 98.0 mm~ 160 mm.
Exact determination of field integral and apex point is affected by the nearby magnet.
To remove these uncertainties, field clamps are installed at the both ends of LGBM1,2.

## Slide 59
ESRF style
Requried #: : 56 + spare
Status : already contracted
Octupole Parameters
 |  | Octupole
B'''= | T/m3 | 240,000
rc= | m | 1.50E-02
Pole to Pole distance= | m | ±0.005
core_len= | m | 0.0740
Leff= | m | 0.0809
NI/pole= | A | 1086.48
Ac= | m2 (2x1mm2) | 2.000E-06
jmax= | A/mm2 | 1.68
I= | A | 3.35
N/coil= | turns | 324
yoke_th= | m | 0.045
L0= | m | 0.298
Ncoil= |  | 4
P/coil= | Watts | 10.12
P (total)= | Watts | 40.49
V= | Volts | 12.07
R= | Ohm | 3.60
Stored Energy (Full 3D model) | Joule | 3.29
L = | Henry | 0.58
Octupole Magnet