## Slide 1
Vacuum System
Taekyun Ha
On be half of Vacuum Group
Nov. 05, 2025
4th Korea-4GSR International Advisory Committee Meeting (Nov. 5-6, 2025)

## Slide 2
CONTENTS
Introduction
I
Linac & Booster Vacuum
I I
Storage Ring Vacuum
I I I
Summary
I V
Linac Vacuum System
Booster Vacuum System
2
Design Strategy
Change Log of Chamber Design
Overview
Design for Low impedance
Photon Absorber and Beam Handling
Vacuum Simulation
Vacuum Chamber Prototyping
Fabrication Schedule

## Slide 3
Layout of Accelerator
I. Introduction
3
4 | GeV
400 | mA
800 | m Ring
Storage Ring
Booster

## Slide 4
Accelerator Vacuum System
I. Introduction
4
Linac vacuum
  Electron beam energy 0  200 MeV
  Four S-band accelerating columns with two modulator-klystron stations
  Photo-cathode E-gun (~10-11 mbar), AC and wave guide (~10-8 mbar)
Booster vacuum
  Electron beam energy 200 MeV  4 GeV
  Circumference ~770 m with 30 cells
  Beam duct OD ∅22.6~32 mm, thickness 0.8 mm (low eddy current)
  Chamber materials: SS316L (0.8 mm-thick)  Max. stress < 2.5 MPa
  Vacuum requirement ~10-8 mbar
Storage ring vacuum
  Electron beam energy 4 GeV & beam current 400 mA
  Circumference ~800 m with 28 cells
  Beam duct Inner diameter ∅18(V) x 24(H) mm
  Vacuum requirement during operation ~10-9 mbar
※ Pressure distribution
w.r.t. pump distance

## Slide 5
Linac Vacuum System
II. Linac & Booster Vacuum System
5
Photo-cathode E-gun:
  Vacuum requirement during operation ~ 10-11 mbar
  Low outgassing vacuum chamber with SIP(1 ea, 60 L/s), NEG cartridges(2 ea, 400 L/s)
Accelerating columns and wave guides
  Four S-band accelerating columns with two modulator-klystron stations
  Vacuum requirement during operation ~ 10-8 mbar
  Five SIPs per module (60 L/s), vacuum interlock with CCG signal
Linac to Booster (LTB): Vacuum requirement during operation ~ 10-8 mbar

## Slide 6
Booster Vacuum System
II. Linac & Booster Vacuum System
6
Circumference ~770 m with 30 cells
Racetrack type beam duct with 33.6 mm (H) x 22.6 mm (V) for magnets
Chamber materials: SS316L (0.7 mm-thick)  Max. stress < 2.5 MPa
Eddy current heating effect < 1 mW/cm2  Negligible temperature rise
Outgassing rate < 1.5x10-10 mbar l/s cm2  Avg. pressure < 5x10-8 mbar
※ Pressure distribution w.r.t. pump distance
※ Chmber crosssection
0.8 mm
※ One cell layout of booster vacuum system

## Slide 7
Design Strategy
III. Storage Ring Vacuum System
7
Distributed pumping system using “Pill-type Getters”
Bake-out & NEG activation in the tunnel (“In-situ bake-out”)
Maximize the exposure of the chamber wall to synchrotron radiation for rapid beam cleaning
Two step installation:
  Pre-assemble magnets and vacuum chambers on a girder outside the tunnel
  Connect the chamber between the two girders using bellows in the tunnel
Low impedance design:
  24x18 octagon-shaped e-beam channel with 4 mm high winglet for synchrotron radiation handling
  Try to make the transition angle less than 1:10
  Bellows and gate valve having RF-shielded finger which is made of thin copper plate with slots
  No components penetrate into the beam channel (cross section change only in the winglet)
SR
e-
Cooling water
Sheath heater
Pill-NEG

## Slide 8
Overview
III. Storage Ring Vacuum System
8
※ Arc-section length: 22.3 m
※ Bending angle (1 Cell): 12.857°
※ 28 cells (800 m)
SR one cell layout
CN01
CN02
CN03
CN04
CN06
CN07
CN08
CN10
CN11
CN12
CN13
SR one cell vacuum chambers
Pill-NEG
Cooling water
Beam chamber
24(H)×18(V)
SR
e-
Photon beam (ID)
Photon beam (BM)
e-
Vacuum chamber cross-section
CN05
CN09
※ 13 vacuum chambers per arc-section

## Slide 9
Design Change of the Vacuum Chamber
III. Storage Ring Vacuum System
9
ID beam
Bending
beam
Pill-NEG
Cooling water
Beam chamber
24(H)×18(V)
SR
e-
ID beam
Bending beam
Conceptual Design (Ver. 1)
SR
e-
SR
e-
Cooling water
Sheath heater
Sheath heater
Pill-NEG
Current Design (Ver. 3)
Modified Design (Ver. 2)

## Slide 10
Improvement of Dynamic Pressure
III. Storage Ring Vacuum System
10
ID beam
Bending
beam
Pill-NEG
Cooling water
Beam chamber
24(H)×18(V)
SR
e-
ID beam
Bending beam
Conceptual Design (Ver. 1)
SR
e-
SR
e-
Cooling water
Sheath heater
Sheath heater
Pill-NEG
Current Design (Ver. 3)
Modified Design (Ver. 2)

## Slide 11
III. Storage Ring Vacuum System
11
CH01
CH02
CH03
CH04
CH06
CH07
CH08
CH10
CH11
CH12
CH13
BPM (10 ea, STS316)
RF-shielded Bellow (10 ea)
Photon absorber (4 ea, OFHC)
Photon mask (3 ea, OFHC)
CH05
CH09
Stainless steel (4 ea)
Aluminum (6 ea, extruded)
Aluminum (3 ea, machined)
Sputter Ion Pump (11 ea, 60 L/s)
NEG Pump (10 ea, 400 L/s)
Ion Gauge (5 ea)
RGA (2ea)
All-metal Angle Valve (2 ea)
RF-shielded Gate Valve (2 ea)
Main Components of the SR Vacuum System

## Slide 12
Design for Low Impedance (RF Shielding)
III. Storage Ring Vacuum System
12
[Comb-type RF shield for gate valve]

## Slide 13
Design for Low Impedance (RF Contact)
III. Storage Ring Vacuum System
13
Bal seal
RF-bridge
Beam current
RF bridge type
Bal seal type
RF heating test at PLS-II Storage ring
Bal seal
RF bridge

## Slide 14
Impedance Budget
III. Storage Ring Vacuum System
14
 |  | Single Component |  | Sum |  | 
Components | Number | kz [V/pC] | Znz [mOhm] | kzT [V/pC] | ZnzT [mOhm] | ZnzT [mOhm]
Resistive Wall | 1 | 14.78 | 158.20 | 14.78 | 158.2 | 158.2
Main RF cavity | 10 | 1.17 | 5.98 | 11.65 | 59.80 | 59.80
LGBM1U chamber | 28 | 2.34E-02 | 0.16 | 0.65 | 4.37 | 4.37
LGBM2D chamber | 28 | 3.42E-02 | 0.34 | 0.96 | 9.39 | 9.39
BPM | 176 | 2.30E-02 | 0.17 | 4.05 | 30.62 | 30.62
Gate valve | 112 | 3.38E-02 | 0.30 | 3.79 | 33.82 | 33.82
ID taper | 26 | 2.56E-03 | 0.89 | 0.07 | 23.17 | 23.17
Bellows | 224 | 7.09E-03 | 0.07 | 1.59 | 15.19 | 15.19
BPM-Bellows 1 | 56 | 2.72E-02 | 0.23 | 1.52 | 12.94 | 12.94
BPM-Bellows 2 | 56 | 2.50E-02 | 0.23 | 1.40 | 12.94 | 12.94
Flange | 840 | 3.00E-05 | 0.02 | 0.03 | 15.96 | 15.96
RF taper | 6 | 7.70E-02 | 1.89 | 0.46 | 11.32 | 11.32
LFS | 1 | 1.58E+00 | 6.30 | 1.58 | 6.30 | 6.30
RF transition chamber | 5 | 8.50E-02 | 0.75 | 0.43 | 3.76 | 3.76
Pump tee | 56 | 5.16E-03 | 0.13 | 0.29 | 7.45 | 7.45
TFS (vert-) | 1 | 1.82E-01 | 0.67 | 0.18 | 0.67 | 0.67
TFS (hori-) | 1 | 1.82E-01 | 0.67 | 0.18 | 0.67 | 0.67
Center bend chamber | 28 | 3.52E-03 | 0.21 | 0.10 | 5.88 | 5.88
CH08 entrance | 56 | 7.90E-04 | 0.03 | 0.04 | 1.68 | 1.68
CH08 exit | 56 | 1.82E-04 | 0.01 | 0.01 | 0.73 | 0.73
Collimator | 4 | TBD |  | TBD |  | 
Total |  |  |  | 44 | 415 | 
Chart: Loss factor
| RW | Main RF | BPM | GateValve | Others | Diagnostics | Bellows | Transitions | Flange
 | 14.78 | 11.65 | 6.9724 | 3.7901 | 2.3259 | 1.946 | 1.587 | 0.68168 | 0.0252
Loss factor Effective
impedance

## Slide 15
Photon Fan and Beam Branch Chamber
III. Storage Ring Vacuum System
15
Photon absorber (mask)
Crotch absorber for the bending beamline
Crotch absorber for the ID beamline
※ SR power density along the ring
(for Φ24 mm uniform beam pipe)

## Slide 16
Photon Fan and Beam Branch Chamber
III. Storage Ring Vacuum System
16
ID | Gap (mm) | λu (mm) | L (m) | B [x/y] (T) | K [x/y/⊥] | Max. Power density (kW/mrad2) | Max. Divergence (mrad)
IVU20 | 5 | 20 | 3 | 0.8867 | 1.6558 | 142 | ± 0.2 (H)
EPU98 | 15 | 98 | 3.6 | H: 0/1.2020 | 0/11/11 | 45 | ± 1.5 (H)
 |  |  |  | V: 0.8015/0 | 7.335/0/7.335 | 30 | ± 1.0 (V)
 |  |  |  | C: 0.6667/0.6675 | 6.1/6.108/8.633 | 12 | ± 0.8 (H,V)
※ Power density profile @ 10 m from the ID center
※ Parameters for typical IDs
IVU20
EPU98 (H mode)
EPU98 (V mode)
EPU98 (C mode)
± 1.5 mrad
± 1.0 mrad
± 0.8 mrad
± 0.2 mrad
± 0.8 mrad
※ Orbit interlock condition of e-BPMs for the ID
  ±0.1 mrad ± 400 μm offset
  (Rms orbit error ~ 150 μm)

## Slide 17
Photon Beam Aperture and Clearance
III. Storage Ring Vacuum System
17

## Slide 18
Thermo-mechanical Analysis
III. Storage Ring Vacuum System
18
Crotch absorber 2 (for the bending beamline)
EPU98 beam
Crotch absorber 1 (for the ID beamline)
[Beam opening]
±1.5 × ±1.0 mrad (H×V)
[PA LGBM1U]
[Photon fan from upstream bending magnets]
[Max. Temperature for EPU98 (Hor. mode)]
[Max. Temperature for EPU98 (Ver. mode)]
[Max. Temperature]
[Photon fan from upstream bending magnets]
SD = 6 m
118℃
[Beam opening]
±1.0 mrad (H)
※ Max stress ~ 70 MPa

## Slide 19
Vacuum Profile Simulation (Ver. 2)
III. Storage Ring Vacuum System
19
Synrad & Molflow simulation
  We assumed the PSD yield of 1E-6 (H2) and 2E-7 (CO)
  Average pressure after fully cleaned ~1×10-9 mbar
Average pressure (1.38 x 10-9 mbar)
Commisioning stage
Fully cleaned stage
1E-9 mbar

## Slide 20
Vacuum Profile Simulation (Ver. 3)
III. Storage Ring Vacuum System
20
5E-11 mbar

## Slide 21
Vacuum Chamber Prototyping (1)
III. Storage Ring Vacuum System
21
Dipole magnet chamber (extruded type, CH12)
1. Extrusion
2. Bending
3. Curvature test
4. Machining
5. Chemical cleaning
8. Assemble & alignment
7. Welding
※ Error < ±0.5 mm
※ He leak rate < 10-10 mbar l/s
6. NEG insertion

## Slide 22
Vacuum Chamber Prototyping (2)
III. Storage Ring Vacuum System
22
Beamline branch chamber (machined type, CH02)
2. Chemical cleaning
3. Welding
4. Assemble & vacuum test
1. Machining
※ He leak rate < 10-10 mbar l/s

## Slide 23
Vacuum Test of Prototype Chamber
III. Storage Ring Vacuum System
23
Al extruded chamber with Pill-NEGs (2 lines)
Baking at 180℃ for 48 h
Base pressure measured at 3 points
Base pressure at the center of the chamber
P2 < 5×10-11 mbar
Measurement set-up
P1
P2
P3
Sheath heaters

## Slide 24
Displacement Test of Prototype Chamber
III. Storage Ring Vacuum System
24

## Slide 25
Displacement Test of Prototype Chamber
III. Storage Ring Vacuum System
25

## Slide 26
Fabrication Schedule (Original)
III. Storage Ring Vacuum System
26
※ Delayed by 8 months from the original schedule

## Slide 27
III. Summary
27
Vacuum system design optimization completed
Estimated vacuum profile: average pressure < 1×10⁻⁹ mbar
Photon absorber thermal analysis completed
Vacuum chamber prototyping and testing completed
First article fabrication initiated for all chamber types

## Slide 28
4th Korea-4GSR International Advisory Committee Meeting (Nov. 5-6, 2025)
Thank You
Notes: 이것으로 기반시설 구축과 관련된 발표를 마치겠습니다. 감사합니다.
발표내용과 관련하여, 질의사항이나 추가 코멘트가 있을 시 말씀해주시면 감사하겠습니다.